## Slide 1: Clustering for High Availability
Module 6: Check Point ClusterXL Instructor: Kim Winfield

## Slide 2: Objectives
Describe the need for High Availability
Clustered Firewalls
Cluster Control Protocol

## Slide 3: High Availability
The need for High Availability commonly referred to as HA
Active/Standby Security Gateways
Load Balanced Security Gateways

## Slide 4: Cluster IP Address
Cluster Members Physical IP address
Virtual IP Address

## Slide 5: Cluster Synchronization
The need for synchronization
Full Synchronization
Delta Synchronization

## Slide 6: Clustered Firewalls
High Availability Cluster
Load Balanced Cluster
VRRP Cluster

## Slide 7: High Availability
Active Standby
New Mode High Availability
VMAC (Virtual MAC Mode)

## Slide 8: New Mode High Availibility
Each member has a unique IP address and unique MAC Address
The Cluster has an Active and a Standby Member
The Active member responds to traffic to the Virtual IP Address or Cluster IP Address
The Cluster IP Address is associated with the MAC Address of the Active Member of the cluster
If a failover occurs the member that becomes active performs a gratuitous ARP broadcast so other members learn of the new MAC adddress

## Slide 9: VMAC (Virtual MAC) Mode
The Cluster has an Active and a Standby Member
Each member has a unique MAC address but the Active Cluster member responds to the Virtual IP address and to the Virtual MAC address
The Cluster IP Address is associated with the Virtual MAC Address
If a failover occurs the member that becomes active responds to traffic sent to the Virtual IP and Virtual MAC Address

## Slide 10: Cluster Control Protocol (CCP)
What is CCP
Broadcast or Multicast

## Slide 11: Cluster Control Protocol (CCP)
Multicast MAC Address
How is the address determined

## Slide 12: Summary
Understand why High Availability is needed for fault tolerant security.
Understand what options are available for Clustered Firewalls
Understand how Cluster Control Protocol is used to monitor firewall state

## Slide 13: Bibliography
Check Point R80.10 ClusterXL Administration Guide California: USA
Tim Hall Security Gateway High Availability California: USA