## Slide 1: Module 7 CoreXL and SecureXL
Module 7: CoreXL and SecureXL Instructor: Kim Winfield

## Slide 2: Objectives
Comprehend the effects of CoreXL for Multiple Core Firewalls
Apply SecureXL for packet and session rate acceleration of firewall traffic
Utilize CoreXL and SecureXL in performance tuning for firewalls

## Slide 3: CoreXL
Firewall Instance
Multiple Core Servers
Leveraging Multiple Firewall Instances for increased performance

## Slide 4: CoreXL
Firewall Instance Replication across multiple core gateways
Example to the right
  3 Firewall Instances
  1 Secure Network Distributor

## Slide 5: CoreXL
Secure Network Distributor
Default distribution of cores
  1 Distributor for 4 core Security Gateways
  2 Distributor for 8 core Security Gateway
Depending on performance issues the number of instances can be changed using cpconfig
Clustered Security Gateways need to have the same number of firewall instances

## Slide 6: SecureXL
Accelerating Traffic that has been inspected by the firewall
State information is maintained
Packet Rate Acceleration
Session Rate Acceleration

## Slide 7: SecureXL
Packet Rate Acceleration
SecureXL Table

## Slide 8: SecureXL
Session Rate Acceleration
Templates
  Source Port is not checked in rulebase so an asterisk replaces the source port
  When packet matches the other 4 fields, a connection is created from the template

## Slide 9: Performance Tuning
Performance Pack
SecureXL Templates
NAT Templates
Delayed Notification

## Slide 10: Performance Tuning
Performance Pack
CoreXL
  fwaffininity.conf
  fw ctl affinity
  fw ctl multik stat

## Slide 11: Performance Tuning
Multi-Queue
  Make Sure SecurXL is enabled
  Make sure that the network interfaces support Multi-Queue
  Examine CPU Utilization
  Examine CPU roles allocation
  Decide if more CPU’s can be allocated to the SND

## Slide 12: Summary
Implemented CoreXL for a multiple core Security Gateway
Implement SecureXL for connection and session rate acceleration
Performance Tuning of Security Gateway by modifying the rulebase, SecureXL and CoreXL

## Slide 13: Bibliography
Check Point R80.10 Security Gateway Technical Administration Guide California: USA
Check Point R80.10 Security Gateway Performance Tuning Administration Guide California: USA